## Slide 1: Arturo Chong Eslava. Phytotecnia Department. Autonomous University of Chapingo achong@correo.chapingo.mx
ASA-CSSA-SSSA
2009 International Annual Meetings
PITSSBURGH
A PROTOTYPE BALANCE MICRO LYSIMETER AS A CONTROL FOR AN IRRIGATION SYSTEM
Introduction. Automatic irrigation systems usually use timers that star and stop pumps or open and close valves at determined times. Soil humidity sensors are also used to star or stop pumps accordingly to their calibration. Although it is possible to control soil humidity of a crop using these methods, they do not integrate plant development and growth and natural evaporation through the plant cycle.
Objectives. To design and built a balance micro lysimeter as a control element of a irrigation system. To probe that natural evaporation can be used to control an irrigation system.
Materials and methods. A balance micro lysimeter was designed to control the irrigation system’s pumps and valves. The micro lysimeter is constructed as two metal boxes, the small one inside the big one. The small one is held by a spring mechanism and contains the soil. As the soil is at field capacity the small box moves down to a minimum and as it looses water it goes up until a chosen maximum. These movements close or open an electric circuit starting or stopping pumps or valves. An irrigated common bean crop was established using the micro lysimeter as a control for watering it.
Selected minimum humidity point or the least lysimeter weight
Pump switch control: ON
Water pump
Water tube to the lysimeter
LYSIMETER
Pump switch control: OFF
Selected maximum humidity point or the highest lysimeter weight
Permanent ON switch
Permanent OFF switch
Figure 1. The metal boxes. The inside box contains the soil and is balanced by metal springs: up & down, as the soil water changes.
Results. The balance micro lysimeter controlled acceptable the water system for the common bean crop, as long as the trial lasted. During raining days, the pump remained off because watering was not needed. At the beginning the switch positions, ON & OFF, needed to be calibrated as well the amount of water that filled the internal box. The water pump was on when the lysimeter weight reached the selected minimum. Common bean growth was acceptable for this initial trial.
Figure 2. General system design. The permanent ON & OFF switches, water pump and the lysimeter.
Conclusion. The evaporation of a crop can be used for watering a crop. A balance micro lysimeter can be used to control an irrigation system.
Figure 3. The common bean crop growing inside the lysimeter during the initial trial.
Black T.A., G. W. Thurtell, and C. B. Tanne. 1968. Hydraulic Load-Cell Lysimeter, Construction, Calibration, and Tests. Soil Sci. Soc. Amer. Proc., Vol. 32. 623-629.
Dugas W.A., Dan R . Upchurch, and Joe T . Ritch. 1985. A weighing lysimeter for evapotranspiration and root measurements. Agronomy Journal. Vol. 77, 821-825.
Heatherly L. G., B. L. McMichael, and L. H. Ginn. 1980. A Weighing lysimeter for use in isolated areas. Agronomy Journal, Vol. 72, 845-847.
Ritchie J.T. and Earl Burnett. 1968. A Precision Weighing Lysimeter for Row Crop Water Use Studies. Agronomy Journal, Vol. 60, September-October. 645-649.